Considerations for Developing a User Requirements Specification

for Serialization (e-Pedigree)

by Jim John, Project Management Quality Consultant, ProPharma Group, Inc.

The starting point for adding Serialization to a packaging line should be the User Requirements Specification.  This provides the basis for the validation of the system by providing the criteria by which the system will be evaluated.  As with any URS an important initial activity is to determine the boundaries of the system we are defining.  When we are considering the implementation of Serialization functionality on a packaging line we need to limit our scope to the development of the information to be captured and the labeling function to document the unit/case/pallet levels of packaging.  The level of labeling – from unit level to pallet level is one of the considerations for determining the extent of the system being developed.  Some of the key URS areas to consider for a serialization system at the Packaging Equipment Level are:

GxP column  - Y/N or X column to recognize whether the requirement is an FDA regulatory requirement (required by predicate rule)

Priority Column  - can be used for Must Have, Important, Nice to Have or other means of prioritizing requirements for bid/implementation purposes.

- Physical Requirements: (Should be consistent with Packaging Line Equipment Requirements)

| Item | Description | Priority | GxP |
| --- | --- | --- | --- |
| 1000 | System shall be capable of applying Serialization information at nn units per minute |  |  |
| 1001 | System shall be capable of applying and verifying Serialization information for units oriented in a (horizontal/vertical) configuration. |  |  |
| 1002 | System shall be designed to apply serialization information for all product container size |  |  |
| 1003 | System must be capable of operating 24 hrs/day, 7 days per week |  |  |
| 1004 | System components and wiring must be labeled |  |  |
| 1005 | Components installed on the line must be cleanable and not interfere with line clearance |  |  |

Note:  Physical Components (Printer, Scanner models) specification should be limited to not constrain Supplier unnecessarily

Operational Requirements

| Item | Description | Priority | GxP |
| --- | --- | --- | --- |
| 2001 | System will have the ability to be turned on or off without affecting the packaging line operation |  |  |
| 2002 | System will allow interruption of Batch without loss of serialization data |  |  |
| 2003 | System security will configurable for Initiation and Close out of Serialization Information |  |  |
| 2004 | System design will allow for Automatic or Manual Application of Label |  |  |
| 2005 | System design will allow for rework of product |  |  |
| 2006 | System can be configured for creation of serial or non-serial labeling. |  |  |
| 2007 | System will allow for restart of suspended/interrupted batches |  |  |
| 2008 | System will transmit reconciliation information to MES System on completion of lot to include: Starting and Ending Serial numbers used Serial Numbers of Series not used (product/label rejected |  |  |
| 2009 | System will include mechanism to verify the serialization ID immediately after application |  |  |
| 2010 | System will provide a reject mechanism for unsuccessful verification with “fail unless positive” logic |  |  |
| 2011 | System will provide information back to the control system on reject to maintain reject count and cause. |  |  |

Control System Requirements

| Item | Description | Priority | GxP |
| --- | --- | --- | --- |
| 3000 | Reject logic will be set up to assume fail unless verification is confirmed |  |  |
| 3001 | Control System will maintain reject count, reject cause and reject serial numbers to communicate to MES System at end of Lot |  |  |
| 3002 | Control System will allow for 3 levels of security: Operation, Supervisor and Maintenance to be applied for key functions |  |  |
| 3003 | Control System will interface with existing MES (electronic batch system) to import serialization information |  |  |
| 3004 | Control System will have UPS backed power |  |  |
| 3005 | System must be capable of maintaining serialization data for the lot in the event of power failure |  |  |
| 3006 | Serialization Control System will communicate with Packaging Line equipment to shut down line in for: Communication failure Consecutive Reject Failures – 3 consecutive failures |  |  |
| 3007 | Serialization Control System will display critical data Total package count Reject Count per Reject Category Fault/Alarm Messages |  |  |

Security Requirements

System shall be designed to allow for 5 levels of security per the security matrix

Security Matrix

| Item | User | Allowed Activity | Priority | GxP |
| --- | --- | --- | --- | --- |
| 4001 | None | Cannot operate the system. |  |  |
| 4002 | Operator | Equipment Operation Fault/Alarm reset View settings |  |  |
| 4003 | Maintenance | Same as Operator Access to maintenance features Train System Change settings Reset Maintenance data |  |  |
| 4004 | Supervisor | Same as Operator and Maintenance Reset Production Data Recipe change selection |  |  |
| 4005 | Administrator | Same as Operator, Maintenance, and Supervisor Change Passwords Access recipe configuration |  |  |

Documentation

| Item | Description | Priority | GxP |
| --- | --- | --- | --- |
| 5001 | Functional Specification will be provided by the Vendor traceable to the URS | High | Y |
| 5002 | Operation and Maintenance Manuals with recommended spare parts and maintenance schedules will be provided in hard and soft copy | High | Y |